Chap7: Floating-Point Support
CP1 in MIPS
Xie Benyi

---
Outline
- Chap4: Floating-Point Support
  - The Exponential/Scientific Notation

---
The Exponential/Scientific Notation
Flag * Mantissa * (Base^Exponent)
1<=...<Base
 2
A Integer

---
The Exponential/Scientific Notation
93 X 10^6
X
Flag * Mantissa * (Base^Exponent)
0.93 X 10^8
1<=...<Base
 2
A Integer
〇
9.3 X 10^7

---
The Exponential/Scientific Notation
Python 2.7
In [9]: math.pow( math.sqrt(10), 2 )
Out[9]: 10.000000000000002
Flag * Mantissa * (Base^Exponent)
1<=...<Base
 2
A Integer
Rounding Nearest
Rounding Up
Rounding Down
Rounding Zero
Rounding Inf

---
Outline
- Chap4: Floating-Point Support
  - The Exponential/Scientific Notation
  - The IEEE 754 Standard – Bring Order to Chaos

---
The IEEE 754 Standard
Institute of Electrical and Electronics Engineers
Internationalize @1989
- Rounding
  - Up	Down	Zero	Nearest
- Exceptional results
  - Invalid	Infinite	Overflow	Underflow	Inexact
  - Sqrt(-1)	1/0	1/3
- Actions
  - NaN	Inf	Inf	Denormalized Rprsnt

---
Outline
- Chap4: Floating-Point Support
  - The Exponential/Scientific Notation
  - The IEEE 754 Standard – Bring Order to Chaos
    - The Coding Format

---
The Coding Format
Sign
Exponent 8|11
Mantissa 23|52
0
1
...
2046
2047
M==0, inf
0
-1022
...
1023
2047
M!=0, NaN
M==0, zero
M[H]==0, quiet
M!=0, Denormalized number
M[H]==1, Signaling

---
The Coding Format

---
Outline
- Chap4: Floating-Point Support
  - The Exponential/Scientific Notation
  - The IEEE 754 Standard – Bring Order to Chaos
    - The Coding Format
    - 2 Trade-Offs in MIPS

---
2 Trade-Offs in MIPS
- Trap would limit pipeline performance.
  - FPU guesses trap or not at the 1st cycle (mostly reliable).
  - Obey the precise exception/Interrupts rule
    - Cause	EPC	SR(BD)
- A strict Compliance to IEEE 754 and Performance
  - e.g. Denormalized number automatically written as 0.
- Both trade-off details are implement-dependent.

---
Outline
- Chap4: Floating-Point Support
  - The Exponential/Scientific Notation
  - The IEEE 754 Standard – Bring Order to Chaos
  - Floating-point Registers, Control/Status Registers

---
Floating-point Registers
- 32 * 32-bit reg, $f0	…	$f31 (MIPS-I has 16 * 64-bit reg)
- SR(SR) set zero, you get MIPS-I operations.
- Even/Odd reg made up a pair for math
- The odd-numbered registers are only referenced when doing loads, stores, and moves between floating-point and integer registers. (E.g. Conversion among floating-point and integer)
- ABIs would be addressed in section 11.2

---
FP Control/Status Registers
Ctc1
GP
Cfc1
Auxiliary Regs

---
FP Control/Status Registers
Condition bits
Compare & Branch
[Speaker Notes: Disadvantage: - Branch had to execute at integer unit - Cant fit in pipeline well Both branch and test Instrus contain 3-bit field that specified which of 8 possible condition bit they will set or test. MIPS-III or Early only one CC, so set zero.]

---
FP Control/Status Registers
Flush to zero/override/to nearest
Denormalized number
[Speaker Notes: Flush to zero: set it, then result to zero, can avoid a unimplemented trap Flush override: have to set with FS, set alone not work. Will replace the oprand/input with zero Flush to nearest: improve accuracy, some denormalized number would be forced to closest normarlized value, e.g. to smallest representable nunber]

---
FP Control/Status Registers
Unimplemented Exception
Following an FPU trap
[Speaker Notes: FPU cannot perform instrus or FPU is not confident it can compliant to IEEE 754 Unimplemented exception will leave the destination reg unaffected & FP cause undefined.]

---
FP Control/Status Registers
V|Z|O|U|I
IEEE Exception Type
[Speaker Notes: V bit 4 Invalid operation Z bit 3 Divide by zero O bit 2 Overflow U bit 1 underflow I bit 0 Inexact Cause: According to last completed FP instru Enable: If set then trap can happen Flag: “Sticky” version of Cause, and are the logical “or” of the exceptional results that have occurred since the register was last cleared. The Flags bits can only be zeroed again by writing FCSR or FEXR.]

---
FP Control/Status Registers
Rounding Mode
0Nearest | 10 | 2↑ | 3↓
[Speaker Notes: V bit 4 Invalid operation Z bit 3 Divide by zero O bit 2 Overflow U bit 1 underflow I bit 0 Inexact Cause: According to last completed FP instru Enable: If set then trap can happen Flag: “Sticky” version of Cause, and are the logical “or” of the exceptional results that have occurred since the register was last cleared. The Flags bits can only be zeroed again by writing FCSR or FEXR.]

---
FP Control/Status Registers
Ctc1
GP
Cfc1
Auxiliary Regs

---
Floating-Point Implementation Reg
Full convert range
Full 64-bit Regs
FC
F64
CPU Support Long/Word/Double/Single
L/W/D/S
Support Paired-single SIMD
Support MIPS-3D
PS
3D
ProcessorID
Revision
[Speaker Notes: FC between FPs | between FP and Int without running out of bits and causing an unimplemented exception 3D&PS Details later ProcessorID : Typically this returns the same value as the integer-side processor ID in the coprocessor zero PRId register. Perhaps more usefully, it should only ever read nonzero if there really is FPU hard- ware available to your program. Before you read it or succeed in running any floating-point operation, you or your OS needs to switch on the “coprocessor 1” enable SR(CU1) in the CP0 “status” register. Revision : This field is at the whim of implementers; it is probably useful to make this field visible to commissioning or test engineers, and you might test it when implementing some bug workaround. Otherwise, software should studiously ignore it.]

---
Outline
- Chap4: Floating-Point Support
  - The Exponential/Scientific Notation
  - The IEEE 754 Standard – Bring Order to Chaos
  - Floating-point Registers, Control/Status Registers
  - Floating-point Instructions

---
FP Instructions Outline
- Load/Store: FP reg <=> Mem
- Move between Regs: FP reg <=> general-purpose regs
- 3-operand arithmetic operations
- Multiply-add operations
- Sign changing
- Conversion operations
- Conditional branch and test
- Paired-single and MIPS-3D

---
Load/Store
- Uninspected & unconverted
- MIPS-I style operate on even regs.
- MIPS-I-II CPUs: extra clock before FP load data is valid, they are not allowed to interlock that data?
- “Synthetic” assembly is prefered, (e.g. l.d better than ldc1)
- Must be aligned.
lwc1
lwc1
lwc1
lwc1
lwc1
ldc1
...
l.d
s.d
swc1
sdc1
...
native
Synthetic
[Speaker Notes: the “synthetic” form is easier to read and can be used for all CPUs. The assembly may use multiple instructions for CPUs that don’t implement the machine instruction. You can use a synthetic load/store operation with any addressing mode that the assembler can understand (as described in section 9.4).]

---
Move between Regs
dmtc1
...
- Int reg <=> FP reg
  - No conversion and no exception
- FP reg <=> FP reg
  - Need to specify type
  - No exception
  - May copy all bit correctly
- Conditional move
mov.d
...
movt.d
movf.d
movz.d
movn.d

---
3-Operand/Mul-Add/Sign/Conversion
- 3-Operand
  - Can cause any IEEE exception and unimplemented trap.
- Mul-Add
  - Save time of rounding and renormalization.
- Sign
  - Only produce invalid trap (e.g. operate on NaN)
- Conversion
  - Can produce IEEE exception
add.d
add.d
div.d
mul.d
sub.d
add.d
madd.d
msub.d
nmadd.d
nmsub.d
add.d
abs.d
neg.d
cvt.d.s

---
Conditional Branch and Test
FCC7-0
bclf cc, label
- Conditional Brach
- Test
  - fs1<fs2 | fs1>fs2
  - fs1==fs2
  - Unordered (NaN)
bclt label
c.cond.d cc, fs1, fs2
c.cond.d fs1, fs2

---
Outline
- Chap4: Floating-Point Support
  - The Exponential/Scientific Notation
  - The IEEE 754 Standard – Bring Order to Chaos
  - Floating-point Registers, Control/Status Registers
  - Floating-point Instructions
  - Instruction Timing Requirements and boost

---
Instru Timing Requirements & Boost
- Normal FP instrus are interlocked.
- Older CPUs not. Compiler, assembler and programmer must care the sequence of instrus and following:
  - Operations on FP control/status regs
  - FP regs <=> general-purpose regs
  - FP regs load
  - Test condition and branch
- Boost
  - Rearrange, Smart Compiler, Visible pipeline to Prgmmer
Affect parallel
Effect late

---
Outline
- Chap4: Floating-Point Support
  - The Exponential/Scientific Notation
  - The IEEE 754 Standard – Bring Order to Chaos
  - Floating-point Registers, Control/Status Registers
  - Floating-point Instructions
  - Instruction Timing Requirements and boost
  - Initialization and Enabling on Demand

---
Initialization & Enabling on Demand
CPU’s SR
Disable all
CPs
CPU’s SR
Disable all
CPs
Read FPU
Implementation
Reg (FIR)
Switch on
FPU (CP1)
Set up FPU
Control/Status
Reg (FCSR)
Y
- Once FPU running, you have to deal with FP regs saved and restore during interrupts and context switches
  - Lazy context switching
    - Disable the FPU when running a new task or a interrupt routine or kernel.
    - On a CU1-unusable trap, mark the task as an FP user and enable the FP before returning to it.

---
Outline
- Chap4: Floating-Point Support
  - The Exponential/Scientific Notation
  - The IEEE 754 Standard – Bring Order to Chaos
  - Floating-point Registers, Control/Status Registers
  - Floating-point Instructions
  - Instruction Timing Requirements and boost
  - Initialization and Enabling on Demand
  - Floating-Point Emulation

---
Floating-Point Emulation
- Low-cost MIPS CPUs sometimes omit FPU
- FP provided by software, 50-300 times slower
  - Soft float by hidden library
  - Trap and emulate
- Compiled-in FP is much more efficient, while emulater has a high overhead on trap handler.

---
Thanks!
Questions?
Xie Benyi

---
Outline
- Chap4: Floating-Point Support
  - The Exponential/Scientific Notation
  - The IEEE 754 Standard – Bring Order to Chaos
  - Floating-point Registers, Control/Status Registers
  - Floating-point Instructions
  - Instruction Timing Requirements and boost
  - Initialization and Enabling on Demand
  - Floating-Point Emulation