Chap12: Debugging MIPS Designs
Xie Benyi 8/26/18

---
Debug Communications by JTAG
- JTAG
  - Joint Test Action Group @1970s
  - an industry standard, used after manufacture
    - verifying designs
    - testing printed circuit boards
- IEEE Standard 1149.1-1990
  - entitled Standard Test Access Port and Boundary-Scan Architecture.

---
EJTAG & JTAG
- EJTAG
  - MIPS defined
  - Recycle the JTAG pins in every Soc
  - A foundation of non-intrusive debug and trace tools
- JTAG
  - A control/data enable input
  - A data-in line
  - A data-out line

---
Requirements
- Physical communications with the host ✔
- The ability to remote-control the CPU
  - Map communication space into host CPU’s vaddr
- Breakpoint regs
  - Map into host CPU’s vaddr
- A just-for-debug exception

---
The dseg Mem Decode Region

---
The dseg Mem Decode Region
- Dseg – the whole debug-only memeory area
  - Dmseg – probe memery region
    - Fastdata – block-mode probe protocol (boost)
    - Debug entry – debug exception entry point
  - Drseg – debug unit’s main regs ★

---
The drseg Mem Decode Region
The DCR (Debug Control) Regs
- Most bits are read-only
- ENM
  - (Read-Only) reports CPU endiannes

---
The drseg Mem Decode Region
EJTAG Breakpoint Hardware
- Monitoring instruction fetch, load, and store access form the CPU.
- Set a breakpoint, if some access matches it for address/data, then comes a debug exception.
- Working on virtual address.

---
The drseg Mem Decode Region
EJTAG Breakpoint Regs
- IBS/DBS – Status
  - IBA/DBA – Address
  - IBM/DBM – address Mask
  - IBASID/DBASID – ASID
  - IBC/DBC – Control
  - DBV(Hi) - Value

---
The drseg Mem Decode Region
EJTAG Breakpoint Regs

---
The drseg Mem Decode Region
EJTAG Breakpoint Regs

---
The drseg Mem Decode Region
DBC(BAI7-0) - Byte Access Ignore
- load/store byte	x111
- load/store halfword	x110
- load/store word	x100
- load/store doubleword	x000
X000
X001
X010
X011
X100
X101
X110
X111

---
The drseg Mem Decode Region
DBC(BAI7-0) - Byte Access Ignore
- What if set DBM as 0111
  - load/store byte	x110	would hit
  - load/store halfword	x100	would hit
  - ...
X000
X001
X010
X011
X100
X101
X110
X111

---
How to enable Breakpoints
Enable
IBC/DBC(BE)
Set IBA/DBA
&
IBM/DBM
Set IBC/DBC(ASIDuse)
&
IBASID/DBASID
Set DBV(Hi)
DBC(BLM)
//data per byte mask
Set DBC(BAI)
Set DBC(NoLB & NoSB)
// No Load Breakpoint
// No Store Breakpoint
It’s quite complicated, but logical.

---
- Physical communications with the host ✔
- The ability to remote-control the CPU ✔
- Breakpoint regs ✔
- A just-for-debug exception

---
Debug regs in CP0
- Debug
- DEPC – restart address (used by deret)
- DSAVE – save a general-purpose reg, so that it can use that reg as an address base to save all the others

---
Debug regs in CP0

---
Use EJTAG by Software
- Debug entry at kseg1
- Sdbbp calling into debug mode inside kernel
- Virtual-address-only breakpoint
- Be care of nested exception and other illegal place

---
MISCs.
- CP0 watchpoint and break instruction
  - Less functions but lots of uninterpreted bits can be implemented by software
- Pdtrace
  - An add-on to the EJTAG, record PC
- Performance Counters

---
Chap12: Debugging MIPS Designs
THANKS!
Xie Benyi 8/26/18